## Slide 1: The AMD Branch (Mis)predictor
New Types and Methods of Straight-Line Speculation (SLS) Vulnerabilities
April 2022
hardwear.io webinar
Pawel Wieczorkiewicz
Open Source Security, Inc.

## Slide 2: whoami
Pawel Wieczorkiewicz
  Email: wipawel@grsecurity.net
  Twitter: @wipawel
Security Researcher at Open Source Security, Inc. (creators of grsecurity®)
  Low-level security research of system software and hardware
  Reverse engineering and binary analysis
Kernel Test Framework (KTF) creator and maintainer
  https://github.com/KernelTestFramework/ktf

## Slide 3: Outline
Theory
  Quick AMD microarchitecture overview
  Branch predictors
    Basic introduction
    Purpose
    Building blocks and functionality
    Different types of branches
  Straight-Line Speculation (SLS)
    Basic introduction
    Root cause mechanics
    Types
Practice
  CVE-2021-26341: a new unexpected type of SLS
    Basic introduction
    Speculation window and its limitations
    SLS gadgets
    Store-to-Load Forwarding (STLF)
  Spectre v1: Fall-thru speculation of conditional branches
    Bounds check latency related out-of-bound array access?
    Branch predictor involvement
    Speculation window and its limitations
  SLS mitigations

## Slide 4: Microarchitecture - overview
AMD Zen2 microarchitecture
source: en.wikichip.org

## Slide 5: Microarchitecture - overview
AMD Zen2 microarchitecture
  Frontend
source: en.wikichip.org

## Slide 6: Microarchitecture - overview
AMD Zen2 microarchitecture
  Frontend
    Fetch
source: en.wikichip.org

## Slide 7: Microarchitecture - overview
AMD Zen2 microarchitecture
  Frontend
    Fetch
    Decode
source: en.wikichip.org

## Slide 8: Microarchitecture - overview
AMD Zen2 microarchitecture
  Frontend
    Fetch
    Decode
    Dispatch
source: en.wikichip.org

## Slide 9: Microarchitecture - overview
AMD Zen2 microarchitecture
  Backend
source: en.wikichip.org

## Slide 10: Microarchitecture - overview
AMD Zen2 microarchitecture
  Backend
    Superscalar
source: en.wikichip.org

## Slide 11: Microarchitecture - overview
AMD Zen2 microarchitecture
  Backend
    Superscalar
    Out-of-order execution
source: en.wikichip.org

## Slide 12: Microarchitecture - overview
AMD Zen2 microarchitecture
  Backend
    Superscalar
    Out-of-order execution
    In-order retire
source: en.wikichip.org

## Slide 13: Microarchitecture - overview
AMD Zen2 microarchitecture
  Frontend
    Fetch
    Decode
    Dispatch
  Backend
    Superscalar
    Out-of-order execution
    In-order retire
source: en.wikichip.org
Frontend
Backend

## Slide 14: Microarchitecture - overview
AMD Zen2 microarchitecture
  Frontend
    Fetch
    Decode
    Dispatch
  Backend
    Superscalar
    Out-of-order execution
    In-order retire
source: en.wikichip.org
Frontend
Backend

## Slide 15: Microarchitecture - overview
AMD Zen2 microarchitecture
  Frontend
    Fetch
    Decode
    Dispatch
  Backend
    Superscalar
    Out-of-order execution
    In-order retire
source: en.wikichip.org
Frontend
Backend

## Slide 16: Branch predictors - purpose
Why do we need the branch prediction unit (BPU)?
  Backend of modern superscalar and out-of-order CPUs can have many instructions “in-flight”
  Frontend must keep up supplying instructions to the Backend
  Any feedback from Backend to Frontend will stall the CPU
    Must be avoided
    Some definitive information available only in the Backend
      Frontend must predict the likely outcome upfront
        Correct prediction  performance win
        Misprediction  penalty, Frontend re-steer when Backend detects
        The better (more accurate) prediction rate, the better performance (fewer bubbles)
  Frontend needs to know where to find next instructions to fetch and decode
    Easy for sequential execution  next instruction
    Problematic upon control flow change (branch)
      Two questions:
        IF – taken or not taken
        Where-to – address of the next instruction

## Slide 17: Branch predictors - design and building blocks
Branch Prediction Unit (BPU)
  Many different designs and categories
    Static vs Dynamic
    One-Level vs Two-level
    Local vs Global
    Adaptive
    Agree
    Hybrid
    Neural (Machine Learning)
      Perceptron-based (AMD Zen2)

## Slide 18: Branch predictors - design and building blocks
Branch Prediction Unit (BPU)
  Many different designs and categories
    Static vs Dynamic
    One-Level vs Two-level
    Local vs Global
    Adaptive
    Agree
    Hybrid
    Neural (Machine Learning)
      Perceptron-based (AMD Zen2)
Prediction based on the actual branch instruction and a pre-defined heuristic:
  Type of branch
    Conditional
    Unconditional
  Branch direction
    Forward
    Backward
Examples:
  Unconditional branches are always taken
  Backward branches taken (loops accuracy)
  Forward branches not taken
Unconditional branches are easier to predict than conditional

## Slide 19: Branch predictors - design and building blocks
Branch Prediction Unit (BPU)
  Many different designs and categories
    Static vs Dynamic
    One-Level vs Two-level
    Local vs Global
    Adaptive
    Agree
    Hybrid
    Neural (Machine Learning)
      Perceptron-based (AMD Zen2)
Prediction based on previous execution results of a given branch
  If taken before, likely to be taken again

## Slide 20: Branch predictors - design and building blocks
Branch Prediction Unit (BPU)
  Many different designs and categories
    Static vs Dynamic
    One-Level vs Two-level
    Local vs Global
    Adaptive
    Agree
    Hybrid
    Neural (Machine Learning)
      Perceptron-based (AMD Zen2)
Prediction based on previous executions results of a given branch
  If taken before, likely to be taken again
    1-bit saturation counter
      Previously taken or not taken

## Slide 21: Branch predictors - design and building blocks
Branch Prediction Unit (BPU)
  Many different designs and categories
    Static vs Dynamic
    One-Level vs Two-level
    Local vs Global
    Adaptive
    Agree
    Hybrid
    Neural (Machine Learning)
      Perceptron-based (AMD Zen2)
Prediction based on previous executions results of a given branch
  If taken before, likely to be taken again
    1-bit saturation counter
      Previously taken or not taken
    2-bit saturation counter
      Four states state machine

## Slide 22: Branch predictors - design and building blocks
Branch Prediction Unit (BPU)
  Many different designs and categories
    Static vs Dynamic
    One-Level vs Two-level
    Local vs Global
    Adaptive
    Agree
    Hybrid
    Neural (Machine Learning)
      Perceptron-based (AMD Zen2)
Prediction is based on a two-dimensional table of 2-bit saturation counters (Branch/Pattern History Table) indexed with branch history register

## Slide 23: Branch predictors - design and building blocks
Branch Prediction Unit (BPU)
  Many different designs and categories
    Static vs Dynamic
    One-Level vs Two-level
    Local vs Global
    Adaptive
    Agree
    Hybrid
    Neural (Machine Learning)
      Perceptron-based (AMD Zen2)
Branch History Table is indexed using a distinct branch history register for each encountered conditional branch

## Slide 24: Branch predictors - design and building blocks
Branch Prediction Unit (BPU)
  Many different designs and categories
    Static vs Dynamic
    One-Level vs Two-level
    Local vs Global
    Adaptive
    Agree
    Hybrid
    Neural (Machine Learning)
      Perceptron-based (AMD Zen2)
Branch History Table is indexed using a distinct branch history register for each encountered conditional branch
Branch History Table is indexed using a shared (global) branch history register for all encountered conditional branches
  Correlation between different branches is considered
  May harm prediction accuracy when too many branches are not correlated

## Slide 25: Branch predictors - design and building blocks
Branch Prediction Unit (BPU)
  Many different designs and categories
    Static vs Dynamic
    One-Level vs Two-level
    Local vs Global
    Adaptive
    Agree
    Hybrid
    Neural (Machine Learning)
      Perceptron-based (AMD Zen2)
gshare – Two-level adaptive predictor with global history buffer
Taken / Not Taken
SNT
ST
WT
WNT
SNT
ST
WT
WNT
SNT
ST
WT
SNT
ST
WT
WNT
WNT
SNT
ST
WT
WNT
Branch Direction Prediction
Branch History Table (BHT)
T
T
N
T
N
N
T
N
T
N
Global History Register (GHR)
Program Counter

## Slide 26: Branch predictors - design and building blocks
Branch Prediction Unit (BPU)
  Many different designs and categories
    Static vs Dynamic
    One-Level vs Two-level
    Local vs Global
    Adaptive
    Agree
    Hybrid
    Neural (Machine Learning)
      Perceptron-based (AMD Zen2)
Consists of multiple different branch prediction mechanisms
Prediction is based on:
  Prediction mechanism that has had highest accuracy in the past
  Combined output of all implemented prediction mechanisms

## Slide 27: Branch predictors - design and building blocks
So far, we have been implicitly focusing on direct conditional branch predictions
  Taken / Not taken
  Question: IF at all

## Slide 28: Branch predictors - design and building blocks
So far, we have been implicitly focusing on direct conditional branch predictions
  Taken / Not taken
  Question: IF at all
What about other branch types?
  Do they need a branch predictor too?

## Slide 29: Branch predictors - design and building blocks
So far, we have been implicitly focusing on direct conditional branch predictions
  Taken / Not taken
  Question: IF at all
What about other branch types?
  Do they need a branch predictor too?
    Yes, they do!
    Question: Where-to

## Slide 30: Branch predictors - design and building blocks
So far, we have been implicitly focusing on direct conditional branch predictions
  Taken / Not taken
  Question: IF branch at all
What about other branch types?
  Do they need a branch predictor too?
    Yes, they do!
    Question: Where-to
  Another important BPU component:
    Branch Target Buffer (BTB)
Branch Target Address 1
Branch Target Address 2
Branch Target Address 3
Branch Target Address N
...
Branch Target Buffer (BTB)
Target Address Prediction

## Slide 31: Branch predictors – branch target buffer
Predicts address of next instructions after the control flow changes because of a branch
Turns out: ALL branch types need BTB!
  Frontend fetches and decodes, but does not execute instructions
  Frontend needs to know where to fetch next instructions from upon a branch
    It must not wait for Backend
      Performance!
  Hence, BPU is a Frontend’s component and leverages BTB to steer Frontend upon branches
Branch Target Address 1
Branch Target Address 2
Branch Target Address 3
Branch Target Address N
...
Branch Target Buffer (BTB)
Target Address Prediction

## Slide 32: Branch predictors – branch target buffer
Analyzing branch instructions addressing is backend’s job
Where-To problem:
  Direct conditional branches:
    Not taken  next instruction
      easy
    Taken  where-to?
      backward, forward, not easy
  Direct unconditional branches:
    Always taken  where?
      backward, forward, not easy
  Indirect unconditional branches:
    Always taken  where?
      backward, forward, not easy
    Target address may change at runtime, not static
      static prediction will not do
      BTB is crucial for performance
Branch Target Address 1
Branch Target Address 2
Branch Target Address 3
Branch Target Address N
...
Branch Target Buffer (BTB)
Target Address Prediction

## Slide 33: Hybrid branch predictor – example

## Slide 34: Hybrid branch predictor – building blocks
Answer: IF

## Slide 35: Hybrid branch predictor – building blocks
Answer: Where-to

## Slide 36: Branch predictors – different types of branches
Direct
  Conditional
    Jumps
      Taken
      Not Taken
  Unconditional
    Jumps
    Calls
Indirect
  Unconditional
    Jumps
    Calls
    Function return

## Slide 37: Branch predictors – different types of branches
Direct
  Conditional
    Jumps
      Taken
      Not Taken
  Unconditional
    Jumps
    Calls
Indirect
  Unconditional
    Jumps
    Calls
    Function return
x86: Jcc $address
  Control flow change to the specified $address, when condition is met
  Condition cc is based on the state of the status flags (EFLAGS register)
    JA – jump if above
      Status flags: CF=0 and ZF=0
    JB – jump if below
      Status flags: CF=1
    JE – jump if equal
      Status flags: ZF=1
    JNE – jump if not equal
      Status flags: ZF=0

## Slide 38: Branch predictors – different types of branches
Direct
  Conditional
    Jumps
      Taken
      Not Taken
  Unconditional
    Jumps
    Calls
Indirect
  Unconditional
    Jumps
    Calls
    Function return
Example (Taken)
xor %rdi, %rdi ; set ZF=1 test %rdi, %rdi ; set ZF=1
je END_LABEL ; if ZF==1 goto END_LABEL mov (%rsi), %rax ; memory load END_LABEL:
mov %rax, (%rsi) ; memory store
a = 0 if (a == 0)
*addr = %rax
else
%rax = *addr

## Slide 39: Branch predictors – different types of branches
Direct
  Conditional
    Jumps
      Taken
      Not Taken
  Unconditional
    Jumps
    Calls
Indirect
  Unconditional
    Jumps
    Calls
    Function return
Example (Not Taken)
mov $1, %rdi
test %rdi, %rdi ; set ZF=0 je END_LABEL ; if ZF==1 goto END_LABEL mov (%rsi), %rax ; memory load END_LABEL:
mov %rax, (%rsi) ; memory store
a = 1 if (a == 0)
*addr = %rax
else
%rax = *addr

## Slide 40: Branch predictors – different types of branches
Direct
  Conditional
    Jumps
      Taken
      Not Taken
  Unconditional
    Jumps
    Calls
Indirect
  Unconditional
    Jumps
    Calls
    Function return
x86: JMP $address
  Unconditional control flow change to the specified $address, without return
  Direct – target address static
    Part of the instruction
  Used by compilers to implement:
    Loops
    Tail calls
    Sharing common code blocks
      Error handling code
    …
  Other uses:
    RAP – jumping over meta-data in code
    Live patching
    …

## Slide 41: Branch predictors – different types of branches
Direct
  Conditional
    Jumps
      Taken
      Not Taken
  Unconditional
    Jumps
    Calls
Indirect
  Unconditional
    Jumps
    Calls
    Function return
x86: CALL $address
  Unconditional control flow change to the specified $address with return
  Direct – target address static
    Part of the instruction
  CALL instruction  push %rip; jmp $address
  Execution flow is expected to resume at the CALL following instruction eventually
  Used by compilers to implement:
    Procedure calls
    Recursive calls
    …
  Other uses:
    __x86.get_pc_thunk.* – position independent code execution helper on i386/i686
    …

## Slide 42: Branch predictors – different types of branches
Direct
  Conditional
    Jumps
      Taken
      Not Taken
  Unconditional
    Jumps
    Calls
Indirect
  Unconditional
    Jumps
    Calls
    Function return
x86: JMP reg (or [mem])
  Unconditional control flow change to the dynamic address specified via register or memory dereference, without return
  Indirect – target address dynamic
    May change at runtime
    Specified by register or memory location
      i386: absolute address
      x64: pc-relative offset
  Used by compilers to implement:
    Tail calls
    Jump tables
    Switch-case
    Virtual function tables (C++)
    Multiway conditional branches

## Slide 43: Branch predictors – different types of branches
Direct
  Conditional
    Jumps
      Taken
      Not Taken
  Unconditional
    Jumps
    Calls
Indirect
  Unconditional
    Jumps
    Calls
    Function return
x86: CALL reg (or [mem])
  Unconditional control flow change to the dynamic address specified via register or memory dereference, with return
  Indirect – target address dynamic
    May change at runtime
    Specified by register or memory location
      i386: absolute address
      x64: pc-relative offset
  Used by compilers to implement:
    Function pointers
    Virtual functions (C++)
    Position independent code

## Slide 44: Branch predictors – different types of branches
Direct
  Conditional
    Jumps
      Taken
      Not Taken
  Unconditional
    Jumps
    Calls
Indirect
  Unconditional
    Jumps
    Calls
    Function return
x86: RET
  Unconditional control flow change to the $address located on stack
  Indirect – target address dynamic
    May change at runtime
    Stored on stack upon function call
  Used by compilers to implement:
    Function returns
    Retpoline
  Does not use BTB, but Return Stack Buffer (RSB) aka Return Address Stack (RAS)

## Slide 45: Straight-Line Speculation (SLS)
Straight-Line Speculation term was coined by Arm
  result of Google SafeSide project research - CVE-2020-13844
  Arm described SLS as a speculative execution past an unconditional change in the control flow: "Straight-line speculation would involve the processor speculatively executing the next instructions linearly in memory past the unconditional change in control flow“
    Initially observed on indirect unconditional branches on Arm CPUs
Shortly after, the SLS was also observed on “some x86 CPUs”
  Also, on indirect unconditional branches
However:
  SLS had to have been observed on x86 CPUs prior to Arm coining the term
    Appearance of traps after RET instructions:
      ~2018: Microsoft Windows
      ~2019: grsecurity®

## Slide 46: Straight-Line Speculation (SLS)
Types of SLS
  Indirect
    Unconditional
      Jump and Call
        JMP/CALL reg
        JMP/CALL [mem]
      Function return
        RET

## Slide 47: Straight-Line Speculation (SLS)
Types of SLS
  Indirect
    Unconditional
      Jump and Call
        JMP/CALL reg
        JMP/CALL [mem]
      Function return
        RET
  What about direct branches?

## Slide 48: CVE-2021-26341 - Direct unconditional branch SLS
AMD x86 CPUs (Zen1 and Zen2 microarchitectures)
  All direct unconditional branch instructions experience SLS vulnerability too!
    JMP $address
    CALL $address
  Branch direction does not matter
    Forward and backward branches suffer from the SLS
  It is possible to trigger the SLS between two co-located hyper-threads
AMD x86 CPU (Zen3 microarchitecture)
  SLS on direct unconditional branches seems to be fixed
  Big design upgrade of the branch predictor unit
  Intentional or accidental?

## Slide 49: CVE-2021-26341 - Direct unconditional branch SLS
SLS code example
; memory address 0 whose access latency allows to observe the speculative execution
0. mov CACHE_LINE_0_ADDR, %rsi
; memory address 1 whose access latency allows to observe the speculative execution
1. mov CACHE_LINE_1_ADDR, %rbx
; flush both cache lines out of cache hierarchy to get a clean state
2. clflush (%rsi)
3. clflush (%rbx)
4. mfence
5. jmp END_LABEL
; memory load to the flushed cache line; it never executes architecturally
6. mov (%rsi / %rbx), %rax
7. END_LABEL:
8. measure CACHE_LINE_0/1_ADDR access time

## Slide 50: Straight-Line Speculation (SLS)
Why would a modern CPU speculate past a direct unconditional branch?
  After all:
    Its target address is static!
      And encoded as part of the instruction!
    There is no latency involved
      Its unconditional – no need to evaluate conditions

## Slide 51: Straight-Line Speculation (SLS)
Why would a modern CPU speculate past a direct unconditional branch?
  After all:
    Its target address is static!
      And encoded as part of the instruction!
    There is no latency involved
      Its unconditional – no need to evaluate conditions
Let’s see why…

## Slide 52: Straight-Line Speculation (SLS) - mechanics

## Slide 53: Straight-Line Speculation (SLS) - mechanics
Branch

## Slide 54: Straight-Line Speculation (SLS) - mechanics
Branch Target Buffer
Branch

## Slide 55: Straight-Line Speculation (SLS) - mechanics
Jump target address
Predicted correctly

## Slide 56: Straight-Line Speculation (SLS) - mechanics
Mispredicted

## Slide 57: Straight-Line Speculation (SLS) - mechanics

## Slide 58: Straight-Line Speculation (SLS) - mechanics

## Slide 59: Straight-Line Speculation (SLS) - mechanics

## Slide 60: Straight-Line Speculation (SLS) - mechanics

## Slide 61: CVE-2021-26341 - Direct unconditional branch SLS
If there is no entry in the BTB (or Return Address Stack (RAS) for RET instructions)
  the branch will be mispredicted and SLS might occur
    Any branch type!
What does it mean?
  we can easily and almost 100% reliably make affected AMD CPUs mispredict any branch …
    Direct or indirect
    Conditional or unconditional
  … and trigger SLS past it.
How?
  We need to make sure the corresponding BTB entry is not present
  Simplest way: flushing entire BTB

## Slide 62: CVE-2021-26341 - Direct unconditional branch SLS
Flushing entire BTB
  Execute a large enough number of the consecutive branches
  Each will take at least one entry in the BTB
  BTB entries can hold up to two branches within the same 64-byte instruction block
    Provided the first branch is a conditional branch
Solution
  Place two unconditional branches within a single cache-line
    Upon execution at least one entry of the BTB will be taken
  Repeat this code construct a NUMBER of times
    Entire BTB overwritten if the NUMBER is equal to or greater than the number of entries of the given BTB
.macro flush_btb NUMBER
; start at a cache-line size aligned address
.align 64
; repeat the code between .rept and .endr
; directives a NUMBER of times
.rept \NUMBER
jmp 1f ; first unconditional jump
.rept 30 ; half-cache-line-size padding
nop
.endr
1: jmp 2f ; second unconditional jump
.rept 29 ; full cache-line-size padding
nop
.endr
2: nop
.endr
.endm

## Slide 63: CVE-2021-26341 - Direct unconditional branch SLS
Speculation window
  up to 8 simple and short (up to 16 bytes) x86 instructions can be speculatively executed
    in practice: 4-5 short x86 instructions that do not compete for execution units
  up to 2 memory loads can be executed speculatively
    the loads (even pre-cached) cannot provide data to the following uops in time
    the loads do get scheduled and can leave traces in cache hierarchy
Limitations
  constructing a full Spectre v1 gadget is not possible with this type of SLS
  Secret data needs to be available in GPR (registers) for the SLS gadget
  or…

## Slide 64: CVE-2021-26341 - Direct unconditional branch SLS
Store-To-Load-Forwarding (STLF)
  Forwarding data of a completed (but not yet retired) stores to the later loads
    Stores are buffered in the Store Queue (WAW and WAR dependencies)
    Later loads must get fresh data either from the Store Queue (if fresh) or memory
Memory loads executed under SLS receive data from the earlier stores to the same address
  STLF enables speculative loads under SLS to execute fast
  Such loads do provide data to their dependent uops
STLF requirements
  Earlier store contains all the load’s bytes (cannot load more)
  CPU uses address bits 11:0 to determine STLF eligibility
  Same address space and ideally same registers, closely grouped together
Notes: WAW – Write after write
i1. R2 <- R4 + R7
i2. R2 <- R1 + R3
i2 tries to write an operand before it is written by i1
WAR – Write after read
i1. R4 <- R1 + R5
i2. R5 <- R1 + R2
i2 tries to write a destination before it is read by i1

## Slide 65: CVE-2021-26341 - Direct unconditional branch SLS
SLS gadget example
asm goto (
"mov $0x4141414141414141, %%rbx\n“
"mov %%rbx, (%0)\n“
"sfence\n“
"lfence\n“
".align 64\n“
"jmp %l[end]\n“
"mov (%0), %%rbx\n“
"and %1, %%rbx\n“
"add %2, %%rbx\n“
"mov (%%rbx), %%ebx\n“
:: "r" (&path), "r" (1UL << bufsiz), "r" (buf)
: "rbx", "memory“
: end);
end:

## Slide 66: Straight-Line Speculation (SLS)
Types of SLS
  Indirect
    Unconditional
      Jump and Call
        JMP/CALL reg
        JMP/CALL [mem]
      Function return
        RET
  Direct
    Unconditional
      Jump and Call
        JMP/CALL $address

## Slide 67: Straight-Line Speculation (SLS)
Types of SLS
  Indirect
    Unconditional
      Jump and Call
        JMP/CALL reg
        JMP/CALL [mem]
      Function return
        RET
  Direct
    Unconditional
      Jump and Call
        JMP/CALL $address
    What about direct conditional branches?

## Slide 68: Speculation of conditional branches
Both paths of conditional branches (taken or not taken) are architecturally legitimate
  Hence, there is no direct conditional branch SLS
  Rather, we speak of a branch fall-through speculation
If a conditional branch is architecturally taken
  It could be speculatively executed as not taken  mispredicted
Typical Spectre v1 situation

## Slide 69: Spectre v1: a fall-thru speculation of conditional branches
Spectre v1 and conditional branches relation
A common Spectre v1 gadget
  Out-of-bound array access
  Speculative bypass of a bound check
  Bound check memory access latency
Most speculation blocking mitigation target “array-based” Spectre v1 gadgets
But, is Spectre v1 really limited to that?

## Slide 70: Spectre v1: a fall-thru speculation of conditional branches
Flush BTB to trigger a fall-thru speculation for a conditional branch
  No condition evaluation considerations necessary
  No memory access (or any other) latency required
  Easy to make any conditional branch mispredict
    Even a trivial one
  Speculative type confusion
    No need for array out-of-bound
Works also on AMD Zen3!
Neither this nor direct unconditional branch SLS affects Intel

## Slide 71: Spectre v1: a fall-thru speculation of conditional branches
Gadget example
; memory address whose access latency allows to observe the mispredictions
0. mov $CACHE_LINE_ADDR, %rsi
; flush the cache line out of cache hierarchy to get a clean state
1. clflush (%rsi)
2. mfence
3. xor %rdi, %rdi ; set ZF=1
4. jz END_LABEL ; if ZF==1 goto END_LABEL
; memory load to the flushed cache line; it never executes architecturally
5. mov (%rsi), %rax
6. END_LABEL:
7. measure CACHE_LINE_ADDR access time

## Slide 72: Spectre v1: a fall-thru speculation of conditional branches
Speculation window
  Noticeably shorter than “regular” Spectre v1 speculation window
  up to 8 simple and short (up to 16 bytes) x86 instructions can be speculatively executed
    in practice: ~5-7 short x86 instructions that do not compete for execution units
  up to 2 memory loads can be executed speculatively
    the loads (must be pre-cached) do provide data to the following uops in time
Constructing a full Spectre v1 gadget is possible
Secret data can be anywhere in memory
Limitations
  Shorter speculation window  fewer instructions
    More difficult to build cache oracle

## Slide 73: SLS Mitigations
Here we discuss SLS mitigation for the following branches:
  Direct unconditional jump
  Indirect unconditional jump
  Function return RET
These three cases are easy to mitigate
  Just put a speculative execution barrier (i.e., serializing or ordering instruction) after
    The shorter the instruction the better
    Never gets executed architecturally
SLS mitigation for direct and indirect unconditional call is not that simple
  At some point control flow resumes execution at an instruction following the call
    The speculative execution barrier gets executed architecturally
    Must not have architectural “side-effects”

## Slide 74: SLS Mitigations
Mitigation for
  Direct unconditional jump
  Indirect unconditional jump
  Function return RET
  INT3 – single byte opcode (0xCC)

## Slide 75: SLS Mitigations

## Slide 76: SLS Mitigations

## Slide 77: SLS Mitigations

## Slide 78: SLS Mitigations

## Slide 79: SLS Mitigations

## Slide 80: SLS Mitigations

## Slide 81: SLS Mitigations

## Slide 82: SLS Mitigations
Mitigation for
  Direct unconditional call
  Indirect unconditional call
  LFENCE - Not good for performance!
  XOR EAX, EAX – complicated!

## Slide 83: SLS Mitigations
Mitigation for
  Direct unconditional call
  Indirect unconditional call
  LFENCE - Not good for performance!
  XOR EAX, EAX – complicated!
XOR EAX, EAX
  Based on compiler post-call behavior assumptions
    Callee-clobbered registers won’t be used without re-write
    Callee-preserved registers are preserved – invariant
    Only return value register (eax) might be abused
  Clearing return value register before the call
    Forces eax value to 0 during SLS
    No arbitrary content of eax

## Slide 84: SLS Mitigations
Mitigation for
  Direct unconditional call
  Indirect unconditional call
  LFENCE - Not good for performance!
  XOR EAX, EAX – complicated!
XOR EAX, EAX
  Complicated:
    Based on compiler assumptions that might not always hold
      Compiler implementation dependent
    Some calling convention ABIs use eax as function input parameter
      Fastcall / regparm(3)
    Variadic functions may use eax as parameter
    Small structures returned via eax + edx
    What to do with:
      CALL eax

## Slide 85: Thank you
Blogs:
https://grsecurity.net/amd_branch_mispredictor_just_set_it_and_forget_it
https://grsecurity.net/amd_branch_mispredictor_part_2_where_no_cpu_has_gone_before
wipawel@grsecurity.net