## Slide 1: To Branch or Not to Branch
Security Implications of x86 Frontend Implementations
October 2022
Hackers to Hackers Conference (H2HC)
Pawel Wieczorkiewicz
Open Source Security, Inc.

## Slide 2: whoami
Pawel Wieczorkiewicz
  Email: wipawel@grsecurity.net
  Twitter: @wipawel
Security Researcher at Open Source Security, Inc. (creators of grsecurity®)
  Low-level security research of system software and hardware
  Reverse engineering and binary analysis
Kernel Test Framework (KTF) creator and maintainer
  https://github.com/KernelTestFramework/ktf

## Slide 3: Outline
Theory
  Quick AMD microarchitecture overview
  Branch predictors
    Basic introduction
    Purpose
    Building blocks and functionality
  Straight-Line Speculation (SLS)
    Basic introduction
    Root cause mechanics
    Types
Practice
  CVE-2021-26341: a new unexpected type of SLS
    Basic introduction
    Speculation window and its limitations
    SLS gadgets
    Store-to-Load Forwarding (STLF)
  SLS mitigations
  Spectre v1: Fall-thru speculation of conditional branches
    Bounds check latency related out-of-bound array access?
    Branch predictor involvement
    Speculation window and its limitations

## Slide 4: Microarchitecture - overview
AMD Zen2 microarchitecture
source: en.wikichip.org

## Slide 5: Microarchitecture - overview
AMD Zen2 microarchitecture
  Frontend
source: en.wikichip.org

## Slide 6: Microarchitecture - overview
AMD Zen2 microarchitecture
  Frontend
    Fetch
source: en.wikichip.org

## Slide 7: Microarchitecture - overview
AMD Zen2 microarchitecture
  Frontend
    Fetch
    Decode
source: en.wikichip.org

## Slide 8: Microarchitecture - overview
AMD Zen2 microarchitecture
  Frontend
    Fetch
    Decode
    Dispatch
source: en.wikichip.org

## Slide 9: Microarchitecture - overview
AMD Zen2 microarchitecture
  Backend
source: en.wikichip.org

## Slide 10: Microarchitecture - overview
AMD Zen2 microarchitecture
  Backend
    Superscalar
source: en.wikichip.org

## Slide 11: Microarchitecture - overview
AMD Zen2 microarchitecture
  Backend
    Superscalar
    Out-of-order execution
source: en.wikichip.org

## Slide 12: Microarchitecture - overview
AMD Zen2 microarchitecture
  Backend
    Superscalar
    Out-of-order execution
    In-order retire
source: en.wikichip.org

## Slide 13: Microarchitecture - overview
AMD Zen2 microarchitecture
  Frontend
    Fetch
    Decode
    Dispatch
  Backend
    Superscalar
    Out-of-order execution
    In-order retire
source: en.wikichip.org
Frontend
Backend

## Slide 14: Microarchitecture - overview
AMD Zen2 microarchitecture
  Frontend
    Fetch
    Decode
    Dispatch
  Backend
    Superscalar
    Out-of-order execution
    In-order retire
source: en.wikichip.org
Frontend
Backend

## Slide 15: Microarchitecture - overview
AMD Zen2 microarchitecture
  Frontend
    Fetch
    Decode
    Dispatch
  Backend
    Superscalar
    Out-of-order execution
    In-order retire
source: en.wikichip.org
Frontend
Backend

## Slide 16: Branch predictors - purpose
Why do we need the branch prediction unit (BPU)?
  Backend of modern superscalar and out-of-order CPUs can have many instructions “in-flight”
  Frontend must keep up supplying instructions to the Backend
  Frontend needs to know where to find next instructions to fetch and decode
    Easy for sequential execution  next instruction
    Problematic upon control flow change (branch)
      Two questions:
        IF – taken or not taken
        Where-to – address of the next instruction
  However, some definitive information (e.g., about actual control flow) available only in the Backend

## Slide 17: Branch predictors - purpose
Why do we need the branch prediction unit (BPU)?
  Backend of modern superscalar and out-of-order CPUs can have many instructions “in-flight”
  Frontend must keep up supplying instructions to the Backend
  Any feedback from Backend to Frontend may stall the CPU
    Must be avoided
      Frontend must predict the likely outcome upfront
        Correct prediction  performance win
        Misprediction  penalty, Frontend re-steer when Backend detects it
        The better (more accurate) prediction rate, the better performance (fewer pipeline bubbles)

## Slide 18: Branch predictors - design and building blocks
Branch Prediction Unit (BPU)
  Many different designs and categories
    Static vs Dynamic
    One-Level vs Two-level
    Local vs Global
    Adaptive
    Agree
    Hybrid
    Neural (Machine Learning)
      Perceptron-based (AMD Zen2)

## Slide 19: Branch predictors - design and building blocks
Branch Prediction Unit (BPU)
  Many different designs and categories
    Static vs Dynamic
    One-Level vs Two-level
    Local vs Global
    Adaptive
    Agree
    Hybrid
    Neural (Machine Learning)
      Perceptron-based (AMD Zen2)
Prediction based on the actual branch instruction and a pre-defined heuristic:
  Type of branch
    Conditional
    Unconditional
  Branch direction
    Forward
    Backward
Examples:
  Unconditional branches are always taken
  Backward cond. branches taken (loops accuracy)
  Forward conditional branches not taken
Unconditional branches are easier to predict than conditional

## Slide 20: Branch predictors - design and building blocks
Branch Prediction Unit (BPU)
  Many different designs and categories
    Static vs Dynamic
    One-Level vs Two-level
    Local vs Global
    Adaptive
    Agree
    Hybrid
    Neural (Machine Learning)
      Perceptron-based (AMD Zen2)
Prediction based on previous execution results of a given branch
  If taken before, likely to be taken again

## Slide 21: Branch predictors - design and building blocks
Branch Prediction Unit (BPU)
  Many different designs and categories
    Static vs Dynamic
    One-Level vs Two-level
    Local vs Global
    Adaptive
    Agree
    Hybrid
    Neural (Machine Learning)
      Perceptron-based (AMD Zen2)
Prediction based on previous execution results of a given branch
  If taken before, likely to be taken again
    1-bit saturation counter
      Previously taken or not taken

## Slide 22: Branch predictors - design and building blocks
Branch Prediction Unit (BPU)
  Many different designs and categories
    Static vs Dynamic
    One-Level vs Two-level
    Local vs Global
    Adaptive
    Agree
    Hybrid
    Neural (Machine Learning)
      Perceptron-based (AMD Zen2)
Prediction based on previous executions results of a given branch
  If taken before, likely to be taken again
    1-bit saturation counter
      Previously taken or not taken
    2-bit saturation counter
      Four states state machine

## Slide 23: Branch predictors - design and building blocks
Branch Prediction Unit (BPU)
  Many different designs and categories
    Static vs Dynamic
    One-Level vs Two-level
    Local vs Global
    Adaptive
    Agree
    Hybrid
    Neural (Machine Learning)
      Perceptron-based (AMD Zen2)
Prediction is based on a two-dimensional table of 2-bit saturation counters (Branch/Pattern History Table) indexed with branch history register (BHR)

## Slide 24: Branch predictors - design and building blocks
Branch Prediction Unit (BPU)
  Many different designs and categories
    Static vs Dynamic
    One-Level vs Two-level
    Local vs Global
    Adaptive
    Agree
    Hybrid
    Neural (Machine Learning)
      Perceptron-based (AMD Zen2)
Branch History Table is indexed using a distinct branch history register (BHR) for each encountered conditional branch

## Slide 25: Branch predictors - design and building blocks
Branch Prediction Unit (BPU)
  Many different designs and categories
    Static vs Dynamic
    One-Level vs Two-level
    Local vs Global
    Adaptive
    Agree
    Hybrid
    Neural (Machine Learning)
      Perceptron-based (AMD Zen2)
Branch History Table is indexed using a shared (global) branch history register (GHR) for all encountered conditional branches
  Pros:
    Correlation between different branches is considered
  Cons:
    May harm prediction accuracy when too many branches are not correlated

## Slide 26: Branch predictors - design and building blocks
Branch Prediction Unit (BPU)
  Many different designs and categories
    Static vs Dynamic
    One-Level vs Two-level
    Local vs Global
    Adaptive
    Agree
    Hybrid
    Neural (Machine Learning)
      Perceptron-based (AMD Zen2)
gshare – Two-level adaptive predictor with global history buffer
Taken / Not Taken
SNT
ST
WT
WNT
SNT
ST
WT
WNT
SNT
ST
WT
SNT
ST
WT
WNT
WNT
SNT
ST
WT
WNT
Branch Direction Prediction
Branch History Table (BHT)
T
T
N
T
N
N
T
N
T
N
Global History Register (GHR)
Program Counter

## Slide 27: Branch predictors - design and building blocks
Branch Prediction Unit (BPU)
  Many different designs and categories
    Static vs Dynamic
    One-Level vs Two-level
    Local vs Global
    Adaptive
    Agree
    Hybrid
    Neural (Machine Learning)
      Perceptron-based (AMD Zen2)
Consists of multiple different branch prediction mechanisms
Prediction is based on:
  Prediction mechanism that has had highest accuracy in the past
  Combined output of all implemented prediction mechanisms

## Slide 28: Branch predictors - design and building blocks
So far, we have been implicitly focusing on direct conditional branch predictions
  Taken / Not taken
  Question: IF – to branch or not to branch 

## Slide 29: Branch predictors - design and building blocks
So far, we have been implicitly focusing on direct conditional branch predictions
  Taken / Not taken
  Question: IF – to branch or not to branch 
What is the address of a next instruction when the branch is taken?

## Slide 30: Branch predictors - design and building blocks
So far, we have been implicitly focusing on direct conditional branch predictions
  Taken / Not taken
  Question: IF – to branch or not to branch 
What is the address of a next instruction when the branch is taken?
What about other branch types?
  Do they need a branch predictor too?

## Slide 31: Branch predictors - design and building blocks
So far, we have been implicitly focusing on direct conditional branch predictions
  Taken / Not taken
  Question: IF – to branch or not to branch 
What is the address of a next instruction when the branch is taken?
What about other branch types?
  Do they need a branch predictor too?
    Yes, they do!
    Question: Where-to – what is the address of the next instruction?

## Slide 32: Branch predictors – branch target buffer
Another important BPU component:
  Branch Target Buffer (BTB)
Branch Target Address 1
Branch Target Address 2
Branch Target Address 3
Branch Target Address N
...
Branch Target Buffer (BTB)
Target Address Prediction

## Slide 33: Branch predictors – branch target buffer
Another important BPU component:
  Branch Target Buffer (BTB)
    Predicts address of next instructions after the control flow changes because of a branch
    Table of branch target addresses
      indexed with a value derived from a current branch’s program counter value (address)
Branch Target Address 1
Branch Target Address 2
Branch Target Address 3
Branch Target Address N
...
Branch Target Buffer (BTB)
Target Address Prediction

## Slide 34: Branch predictors – branch target buffer
Turns out: ALL branch types need BTB! Why?
  Frontend fetches and decodes, but does not execute (nor specifically analyses) instructions
    With a few exceptions, e.g.:
      int3 - #BP debug exception
      call 0h – get PC thunk
  Upon a branch, frontend needs to know (instantly) where to fetch next instructions from
    It must not wait for Backend  Performance!
Hence, BPU is frontend’s component and leverages BTB to steer frontend upon branches
Branch Target Address 1
Branch Target Address 2
Branch Target Address 3
Branch Target Address N
...
Branch Target Buffer (BTB)
Target Address Prediction

## Slide 35: Branch predictors – branch target buffer
Analyzing exact branch instructions’ addressing is backend’s job
The Where-to problem:
  Direct conditional branches:
    Not taken  next instruction
      easy
    Taken  where-to?
      backward? forward? not easy
  Direct unconditional branches:
    Always taken  where-to?
      backward? forward? not easy
  Indirect unconditional branches:
    Always taken  where-to?
      backward? forward? not easy
    Target address may change at runtime, not static
      static prediction will not do
      BTB is crucial for performance
Branch Target Address 1
Branch Target Address 2
Branch Target Address 3
Branch Target Address N
...
Branch Target Buffer (BTB)
Target Address Prediction

## Slide 36: Hybrid branch predictor – building blocks diagram

## Slide 37: Hybrid branch predictor – building blocks diagram – Taken/Not Taken
Answer: IF

## Slide 38: Hybrid branch predictor – building blocks diagram – Where-to
Answer: Where-to

## Slide 39: Straight-Line Speculation (SLS) - introduction
Straight-Line Speculation term was coined by Arm
  result of Google SafeSide project research - CVE-2020-13844
  Arm described SLS as a speculative execution past an unconditional change in the control flow: "Straight-line speculation would involve the processor speculatively executing the next instructions linearly in memory past the unconditional change in control flow“
    Initially observed on indirect unconditional branches on Arm CPUs
Shortly after, the SLS was also observed on “some x86 CPUs”
  Also, on indirect unconditional branches
However:
  SLS had to have been observed on x86 CPUs prior to Arm coining the term
    Appearance of traps after RET instructions:
      ~2018: Microsoft Windows
      ~2019: grsecurity

## Slide 40: Straight-Line Speculation (SLS)
Types of SLS
  Indirect
    Unconditional
      Jump and Call
        JMP/CALL reg
        JMP/CALL [mem]
      Function return
        RET

## Slide 41: Straight-Line Speculation (SLS)
Types of SLS
  Indirect
    Unconditional
      Jump and Call
        JMP/CALL reg
        JMP/CALL [mem]
      Function return
        RET
  What about direct branches?

## Slide 42: CVE-2021-26341 - Direct unconditional branch SLS
AMD x86 CPUs (Zen1 and Zen2 microarchitectures)
  All direct unconditional branch instructions experience SLS vulnerability too!
    JMP $relative_offset
    CALL $relative_offset
  Branch direction does not matter
    Both forward and backward branches suffer from SLS
  It is possible to trigger SLS between two co-located hyper-threads
AMD x86 CPU (Zen3 microarchitecture)
  SLS on direct unconditional branches seems to be fixed
  Big design upgrade of the branch predictor unit
  Intentional or accidental?

## Slide 43: CVE-2021-26341 - Direct unconditional branch SLS
Why would a modern CPU speculate past a direct unconditional branch?
  After all:
    Its target address is static!
      And encoded as part of the branch instruction!
    There is no latency involved
      It is unconditional – no need to spend time on evaluating any conditions
Let’s see why…

## Slide 44: Straight-Line Speculation (SLS) - mechanics

## Slide 45: Straight-Line Speculation (SLS) - mechanics
Branch

## Slide 46: Straight-Line Speculation (SLS) - mechanics
Branch Target Buffer
Branch

## Slide 47: Straight-Line Speculation (SLS) - mechanics
Jump target address
Predicted correctly

## Slide 48: Straight-Line Speculation (SLS) - mechanics
Mispredicted

## Slide 49: Straight-Line Speculation (SLS) - mechanics

## Slide 50: Straight-Line Speculation (SLS) - mechanics

## Slide 51: Straight-Line Speculation (SLS) - mechanics

## Slide 52: Straight-Line Speculation (SLS) - mechanics

## Slide 53: CVE-2021-26341 - Direct unconditional branch SLS
If there is no entry in the BTB (or Return Address Stack (RAS) for RET instructions)
  the branch will be mispredicted and SLS might occur
    Any branch type!
What does it mean?
  We can easily and almost 100% reliably make affected AMD CPUs mispredict any branch …
    Direct or indirect
    Conditional or unconditional
  … and trigger SLS past it.
How?
  We need to make sure the corresponding BTB entry is not present
  Simplest way: flushing entire BTB

## Slide 54: CVE-2021-26341 - Direct unconditional branch SLS
Flushing entire BTB
  Execute a large enough number of consecutive branches
  Each will take at least one entry in the BTB
  BTB entries can hold up to two branches within the same 64-byte instruction block
    Provided the first branch is a conditional branch
Solution
  Place two unconditional branches within a single cache-line
      Upon execution at least one entry of the BTB will be taken
  Repeat this code construct a NUMBER of times
      Entire BTB overwritten if the NUMBER is equal to or greater than the number of entries of the given BTB
  Or… (ab)use Spectre v2 mitigations
      Trigger IBPB
        via MSR write or by context/privilege switch
.macro flush_btb NUMBER
; start at a cache-line size aligned address
.align 64
; repeat the code between .rept and .endr
; directives a NUMBER of times
.rept \NUMBER
jmp 1f ; first unconditional jump
.rept 30 ; half-cache-line-size padding
nop
.endr
1: jmp 2f ; second unconditional jump
.rept 29 ; full cache-line-size padding
nop
.endr
2: nop
.endr
.endm

## Slide 55: CVE-2021-26341 - Direct unconditional branch SLS
Speculation window
  up to 8 simple and short (up to 16 bytes) x86 instructions can be speculatively executed
    in practice: 4-5 short x86 instructions that do not compete for execution units
  up to 2 memory loads can be executed speculatively
    the loads (even pre-cached) cannot provide data to the following µops in time
    the loads do get scheduled and can leave traces in cache hierarchy
Limitations
  constructing a full Spectre v1 gadget is not possible with this type of SLS
  Secret data needs to be available in GPR (registers) for the SLS gadget
  or…

## Slide 56: CVE-2021-26341 - Direct unconditional branch SLS
Store-To-Load-Forwarding (STLF)
  Forwarding data of a completed (but not yet retired) stores to the later loads
    Stores are buffered in the Store Queue (WAW and WAR dependencies)
    Later loads must get fresh data either from the Store Queue (if fresh) or memory
Memory loads executed under SLS receive data from the earlier stores to the same address
  STLF enables speculative loads under SLS to execute fast enough
  Such loads do provide data to their dependent µops!
STLF requirements
  Earlier store contains all the load’s bytes (cannot load more than has been stored)
  CPU uses memory load address bits 11:0 to determine STLF eligibility
  Same address space and ideally same registers, closely grouped together
Notes: WAW – Write after write
i1. R2 <- R4 + R7
i2. R2 <- R1 + R3
i2 tries to write an operand before it is written by i1
WAR – Write after read
i1. R4 <- R1 + R5
i2. R5 <- R1 + R2
i2 tries to write a destination before it is read by i1

## Slide 57: CVE-2021-26341 - Direct unconditional branch SLS
Direct unconditional branch SLS with STLF gadget PoC example
asm goto (
"mov $0x4141414141414141, %%rbx\n“
"mov %%rbx, (%0)\n“
"sfence\n“
"lfence\n“
".align 64\n“
"jmp %l[end]\n“
"mov (%0), %%rbx\n“
"and %1, %%rbx\n“
"add %2, %%rbx\n“
"mov (%%rbx), %%ebx\n“
:: "r" (&path), "r" (1UL << bufsiz), "r" (buf)
: "rbx", "memory“
: end);
end:
wipawel@pawel-poc:~$ time taskset -c 2 ./readlink Baseline: 200
Secret: 4141414141414141
Result: 0000ffffffffff40
Result: 0000ffffffefff40
Result: 0000fdffffefff40
Result: 0000fdffffeff740
Result: 0000fddfffeff740
Result: 0000fddbffeff740
Result: 0000fddbfbeff740
Result: 0000fddbfbe7f740
Result: 0000fd5bfbe7f740
Result: 0000fd5b7be7f740
Result: 0000fd5b7be7f540
Result: 0000fd5b7be7e540
Result: 0000fd5b7be5e540
Result: 0000fd5b7be1e540
Result: 0000fd5b7be1c540
Result: 0000fd4b7be1c540
Result: 0000fd437be1c540
Result: 0000f5437be1c540
Result: 0000f5437bc1c540
Result: 0000f5417bc1c540
Result: 0000f54179c1c540
Result: 0000f54169c1c540
Result: 0000e54169c1c540
Result: 0000c54169c1c540
Result: 0000c5416941c540
Result: 0000c5414941c540
Result: 0000c54149414540
Result: 0000c54149414140
Result: 0000c14149414140
Result: 0000414149414140
Result: 0000414141414140
real 0m14.620s user 0m11.650s sys 0m2.875s

## Slide 58: CVE-2021-26341 - Direct unconditional branch SLS
Vulnerable pipeline
Pipeline leak
Source: Nord Stream natural gas pipelines spring multiple leaks | Oil & Gas Journal (ogj.com)
Source: https://p0.pxfuel.com/preview/170/208/982/gas-production-technology-power.jpg

## Slide 59: SLS Mitigations
First, we discuss SLS mitigation for the following branches:
  Direct unconditional jump
  Indirect unconditional jump
  Function return RET
These three cases are easy to mitigate
  Just follow them with a speculative execution barrier (i.e., serializing or ordering instruction)
    The shorter the barrier instruction the better
    Never gets executed architecturally
SLS mitigation for direct or indirect call is not that simple
  At some point control flow resumes execution at an instruction following the call
    The speculative execution barrier does get executed architecturally
    Should be fast and must not have architectural “side-effects”

## Slide 60: SLS Mitigations – jumps and rets
The simplest yet effective and therefore commonly used mitigation for
  Direct unconditional jump
  Indirect unconditional jump
  Function return RET
  is the INT3 instruction
    single byte opcode (0xCC)
    #BP exception generation caught at the decode stage in the frontend
What does it look like in action?

## Slide 61: SLS Mitigations – jumps and rets

## Slide 62: SLS Mitigations – jumps and rets

## Slide 63: SLS Mitigations – jumps and rets

## Slide 64: SLS Mitigations – jumps and rets

## Slide 65: SLS Mitigations – jumps and rets

## Slide 66: SLS Mitigations – jumps and rets

## Slide 67: SLS Mitigations – jumps and rets

## Slide 68: SLS Mitigations - calls
What is an optimal SLS mitigation for calls?
  Direct unconditional call
  Indirect unconditional call
LFENCE
  No architectural “side-effects”
  Memory ordering and/or serializing instructions
    Gets executed architecturally after every call - not good for performance!
XOR EAX, EAX
  Wait, what!?
  It’s complicated…

## Slide 69: SLS Mitigations - calls
XOR EAX, EAX
  Idea based on compiler post-call behavior assumptions
    Callee-clobbered registers won’t be used without a re-write
    Callee-preserved registers are preserved – invariant
    Return value register (eax) is assumed to be modified by the callee code
     Hence, under SLS, only return value register (eax) might be abused
  Clearing return value register before the call is sufficient as a mitigation
    Forces eax value to 0 during SLS instead of a potentially arbitrary content

## Slide 70: SLS Mitigations - calls
XOR EAX, EAX
  Why is it complicated?
    Based on compiler behavior assumptions that might not always hold
      Compiler implementation dependent
    Some calling convention ABIs use return value register (eax) as function input parameter
      Fastcall / regparm(3)
    Variadic functions may use eax as parameter
    Functions may return small structures via eax + edx registers
    What to do with:
      CALL eax

## Slide 71: Straight-Line Speculation (SLS)
Types of SLS
  Indirect
    Unconditional
      Jump and Call
        JMP/CALL reg
        JMP/CALL [mem]
      Function return
        RET
  Direct
    Unconditional
      Jump and Call
        JMP/CALL $rel_offset

## Slide 72: Straight-Line Speculation (SLS)
Types of SLS
  Indirect
    Unconditional
      Jump and Call
        JMP/CALL reg
        JMP/CALL [mem]
      Function return
        RET
  Direct
    Unconditional
      Jump and Call
        JMP/CALL $rel_offset
    What about direct conditional branches?

## Slide 73: Speculation of conditional branches
Both paths of conditional branches (taken or not taken) are architecturally legitimate
  Hence, there is no direct conditional branch SLS
  Rather, we speak of a branch fall-through speculation
Assuming a conditional branch is architecturally taken
  When mispredicted  Its not taken path could be speculatively executed too
Such conditional branch fall-through speculation may lead to Spectre v1-like vulnerability situations

## Slide 74: Fall-through speculation of conditional branches
AMD x86 CPUs (Zen1, Zen2 and Zen3 microarchitectures)
  All conditional branch instructions may experience a fall-through speculation
    Root-cause similar to the direct unconditional branch SLS
      When BPU mispredicts or otherwise mis-detects the conditional branch
        No BTB entry for the branch instruction  fall-through speculation
    Even very simple conditional branches with trivially evaluated conditions are susceptible!
  Branch direction does not matter
    Both forward and backward branches suffer from the fall-through speculation
  It is possible to trigger the fall-through speculation between two co-located hyper-threads
  AMD Zen3, despite its significant BPU upgrade, still affected

## Slide 75: Spectre v1 vs fall-through speculation of conditional branches
Speculation window
  Noticeably shorter than “regular” Spectre v1 speculation window
  up to 8 simple and short (up to 16 bytes) x86 instructions can be speculatively executed
    in practice: ~5-7 short x86 instructions that do not compete for execution units
  up to 2 memory loads can be executed speculatively
    the loads (must be pre-cached) do provide data to the following µops in time
Constructing a full Spectre v1 gadget is possible
Secret data can be anywhere in memory
Limitations
  Shorter speculation window  fewer instructions
    More difficult to build cache oracle

## Slide 76: Spectre v1 vs fall-through speculation of conditional branches
It is Spectre v1 again! What’s the big deal?!
A “classic” Spectre v1 gadget is believed to have the following components:
  Out-of-bound array access
  Speculative bypass of a bound check
  Bound check memory access latency
Most of the implemented mitigations target “array-based” Spectre v1 gadgets only
But is Spectre v1 really limited to its “classical” form?

## Slide 77: Spectre v1 vs fall-through speculation of conditional branches
If there is no entry in the BTB
  The conditional branch will be mispredicted and fall-through speculation might occur
    Regardless of the condition and its evaluation latency!
    No bound check memory access required!
    No out-of-bound array access required either!
  Easy to make any conditional branch mispredict
    Even the most trivial one
    Context or privilege level separation does not help
      User-land can flush BTB, and kernel-land code execution will speculate
      Enabled Spectre v2 mitigations might already flush the BTB (e.g., IBPB)

## Slide 78: Spectre v1 vs fall-through speculation of conditional branches
Other Spectre v1 gadget types – Speculative Type Confusion
  Paper: "An Analysis of Speculative Type Confusion Vulnerabilities in the Wild“ by Kirzner and Morrison
  Definition:
    Conditional branch misprediction leading to speculative execution of code with variables holding values of the wrong type and thereby leaking potentially arbitrary memory content
  Source of such gadgets
    Attacker-introduced (e.g., via eBPF)
    Compiler-introduced (compilers might not consider conditional branch mispredictions)
    Code objects polymorphism-related

## Slide 79: Spectre v1 vs fall-through speculation of conditional branches
Spectre v1: Bound Check Bypass
if (x < array1_len) { // branch mispredict: taken
y = array1[x]; // read out of bounds
z = array2[y * 4096]; // leak y over cache channel
}
Spectre v1: Speculative Type Confusion
// ptr argument held in x86 register %rsi
void syscall_helper(cmd_t* cmd, char* ptr, long x) {
cmd_t c = *cmd; // cache miss
if (c == CMD_A) { // branch mispredict: taken
... code during which x moves to %rsi ...
}
if (c == CMD_B) { // branch mispredict: taken
y = *ptr; // read from addr x (now in %rsi)
z = array[y * 4096]; // leak y over cache channel
}
... rest of function ...

## Slide 80: Spectre v1 vs fall-through speculation of conditional branches
Compiler-introduced gadget example
First “if” block modifies the register holding a trusted pointer with an untrusted value of x
  Compiler assumes that if first “if” block executes (CMD_A) the second “if” block will not execute (CMD_B) and vice versa
Easy to make both “if” blocks to execute altogether speculatively by forcing both conditional branches to mispredict (e.g., by flushing BTB)!
   Full Spectre v1 gadget with attacker-controlled arbitrary memory location to be leaked
Spectre v1: Speculative Type Confusion
// ptr argument held in x86 register %rsi
void syscall_helper(cmd_t* cmd, char* ptr, long x) {
cmd_t c = *cmd; // cache miss
if (c == CMD_A) { // branch mispredict: taken
... code during which x moves to %rsi ...
}
if (c == CMD_B) { // branch mispredict: taken
y = *ptr; // read from addr x (now in %rsi)
z = array[y * 4096]; // leak y over cache channel
}
... rest of function ...

## Slide 81: Spectre v1 vs fall-through speculation of conditional branches
Comparing to the bound check bypass:
  Branch condition and its evaluation latency is irrelevant
  There is no array access bound check
  Automatic Spectre v1 gadget detection and mitigation is very hard
    Both conditions depend on neither the trusted pointer nor the untrusted attacker-controlled data
  Difficult to spot the potential vulnerability during manual code audit
Spectre v1: Speculative Type Confusion
// ptr argument held in x86 register %rsi
void syscall_helper(cmd_t* cmd, char* ptr, long x) {
cmd_t c = *cmd; // cache miss
if (c == CMD_A) { // branch mispredict: taken
... code during which x moves to %rsi ...
}
if (c == CMD_B) { // branch mispredict: taken
y = *ptr; // read from addr x (now in %rsi)
z = array[y * 4096]; // leak y over cache channel
}
... rest of function ...

## Slide 82: Spectre v1 vs fall-through speculation of conditional branches
Conditional branch fall-through speculation PoC example
asm volatile(
"xor %%r15, %%r15\n“
"jz 1f\n“
"mov (%0), %%rsi\n“
"and %%rcx, %%rsi\n“
"add %1, %%rsi\n“
"mov (%%rsi), %%eax\n“
"1: nop\n“
:: "r" (pathname),"r" (buf), "c" (1UL << bufsiz)
: "r15", "rsi", "eax", "memory");
wipawel@pawel-poc:~$ sudo sysctl -w kernel.core_pattern="AAAAAAAAAAAAAAAA“
kernel.core_pattern = AAAAAAAAAAAAAAAA
wipawel@pawel-poc:~$ time taskset -c 2 ./readlink
Baseline: 170
Result: 0000fdf7ffffffc0
Result: 0000e9f7ffffffc0
Result: 0000c977fbefebc0
Result: 0000c977f3efebc0
Result: 0000c957f3efebc0
Result: 0000c957f3efe3c0
Result: 0000c957f36fe3c0
Result: 0000c9555145e3c0
Result: 0000c9514141e3c0
Result: 0000c951414163c0
Result: 0000c951414143c0
Result: 0000c941414143c0
Result: 0000c141414143c0
Result: 00004141414141c0
Result: 0000414141414140
real 0m0.338s user 0m0.338s sys 0m0.000s

## Slide 83: Thank you
Blogs:
https://grsecurity.net/amd_branch_mispredictor_just_set_it_and_forget_it
https://grsecurity.net/amd_branch_mispredictor_part_2_where_no_cpu_has_gone_before
wipawel@grsecurity.net